## Slide 1: Differences Between GPRS, EDGE, 3g, HSPA, HSPA+ And 4g LTE
TY ICC Batch-2 Group-1 Seminar Presentation
  Aditya Rothithor- 27
  Adarsh Sapkal- 32
  Shaunak Deshpande- 39
  Shrawani Shinde- 46

## Slide 2: Individual Contribution
Topic | Name
EDGE | Aditya
3G,4G | Adarsh
HSPA, HSPA+ | Shaunak
GPRS | Shrawani

## Slide 3: Literature Survey: HSPA
High Speed Packet Access (HSPA) is an amalgamation of two mobile protocols, High Speed Downlink Packet Access (HSDPA) and High Speed Uplink Packet Access (HSUPA), that extends and improves the performance of 3G mobile telecommunication networks. The first HSPA specifications supported increased peak data rates of up to 14 Mbit/s in the downlink and 5.76 Mbit/s in the uplink[1].
HSDPA was first introduced in 2005, and it allowed networks based on the Universal Mobile Telecommunications System (UMTS) to have higher data speeds and capacity, and decreased latency and therefore decreased round-trip time for applications.
HSUPA was specified and standardized in 2008, to improve the uplink data rate to 5.76 Mbit/s, extending the capacity, and reducing latency. Together with additional improvements, this creates opportunities for a number of new applications including VoIP, uploading pictures, and sending large e-mail messages.

## Slide 4: Literature Survey: HSPA+
Evolved High Speed Packet Access, or HSPA+, is a technical standard for wireless broadband telecommunication. It is the second phase of HSPA which has been introduced in 3GPP release 7 and further improved in later 3GPP releases. HSPA+ can achieve data rates of up to 42.2 Mbit/s, and shows even lesser latency than HSPA.
HSPA+ is a further enhancement that introduces higher-level modulation techniques such as 16-state quadrature amplitude modulation (16QAM) and 64-state QAM (64QAM) in the uplink and downlink respectively to replace the standard quadrature phase-shift keying (QPSK) modulation of the base W-CDMA standard.[2]

## Slide 5: Possible questions on the topic
What is the difference between UMTS (regular 3G) and HSPA?
What is difference between HSPA & HSPA+?
What are the two main components of HSPA?
Why is generally uplink speed lesser than downlink speed?
Why does latency matter in networking?

## Slide 6: References
“HSPA” GSMA, www.gsma.com archived on 12-07-2012.
3G Release 7 - See version 7 of ’Technical Specifications and Technical Reports for a UTRAN-based 3GPP system’, TR 21.101.